The INA226 measures the voltage drop across a shunt resistor, and from that calculates the current using Ohm’s law (I = V/R). Since the INA226 can measure a maximum shunt voltage of 81.92mV (with a resolution of 2.5µV), the maximum current is dependent on the resistance of the shunt.
Below is a table of suggested shunts.
Default R100 – 0R1 ohm ~ 1.3 Amps

Shunt Resistance	Max Current (A)	Part Size	Part Number	Power Rating (W)	Max Power (W)
0.003	27.31	2512	ERJMS4SF3M0U	3	2.24
0.004	20.48	2512	ERJMS4SF4M0U	3	1.68
0.005	16.38	2512	ERJMS4HF5M0U	3	1.34
0.006	13.65	2512	ERJMS4HF6M0U	3	1.12
0.007	11.70	2512	ERJMS4HF7M0U	2	0.96
0.008	10.24	2512	ERJMS4HF8M0U	2	0.84
0.009	9.10	2512	ERJMS4HF9M0U	2	0.75
0.010	8.19	2512	ERJMS4HF10MU	2	0.67